# Commercial Road and Doggett Street Intersection Upgrade

# Newstead

## Project Newsletter December 2019

Brisbane City Council is planning to upgrade the Commercial Road and Doggett Street intersection to improve overall intersection operation and safety for all road users.

This intersection has been identified by Council as requiring safety improvements, particularly for pedestrian movements across Commercial Road due to the large volume of pedestrians in the area.

In addition, a total of seven crashes were reported at the intersection between April 2013 and June 2019, which resulted in three hospitalisations, three requiring medical treatment and one minor injury.

The project will involve signalising the intersection to provide controlled pedestrian crossing facilities and formalise right-turn movements for both west and eastbound traffic on Commercial Road. A right-turn pocket will also be introduced on the southern approach of Doggett Street.

Due to the signalisation there will be changes to on-street parking in the area surrounding the intersection and changes to line marking at the Longland Street and Doggett Street intersection. Additionally, bike boxes will be introduced on the Commercial Road approaches of the intersection to facilitate cycle users.

## Project features

- Signalising the intersection with traffic lights and controlled pedestrian crossing facilities

- Extending the right-turn pocket, west and eastbound, on Commercial Road

- Installing a right-turn pocket southbound on Doggett Street

- Converting Doggett Street to a oneway street for northbound traffic only, between Commercial Road and Longland Street

- Removal of four on-street parking bays on Doggett Street and six on-street parking bays on Commercial Road

- Relocation of the Australia Post box and loading zone on Commercial Road

- Installing on-road bike boxes on Commercial Road at the intersection

- Kerb and channel works

- Resurfacing and line marking.

## This is Brisbetter

Brisbane just keeps getting better. We’re making better flowing roads with the Better Roads for Brisbane plan.

To find out more ways we’re making Brisbane better, visit Council’s website and search ‘Brisbetter’.

## Community feedback

Key themes raised during consultation, with Council’s response detailed below:

| Key community feedback | Council’s consideration and response |
| --- | --- |
| Traffic signals preferred option over a roundabout | The signalised intersection provides safe and controlled movements for all road users. The project will provide right-turn pockets for turning vehicles to allow motorists to wait safely for the green arrow without impacting through traffic movements. A signalised intersection provides safe and controlled pedestrian crossing facilities. A roundabout is not preferred in this location due to the high volume of pedestrians crossing the intersection. Additionally, the land required for a roundabout is not feasible without significant property resumption. |
| Pedestrian connectivity | The existing two zebra crossings will be replaced with controlled signalised crossings on the four approaches to the intersection. The project proposes to introduce a signalised scramble crossing, which allows pedestrians to cross the intersection in all directions at the one time. This will also help to improve safety by removing potential conflicts between vehicles and pedestrians and reduce wait times at the intersection for pedestrians and motorists. |
| Increased traffic in local streets with Doggett Street converted to one-way | The project proposes to convert Doggett Street to oneway for northbound traffic, between Commercial Road and Longland Street. This will address safety concerns through this narrow section of Doggett Street and will ease congestion impacts at the Commercial Road intersection. Motorists are encouraged to use either Kyabra Street or Masters Street to travel southbound towards Commercial Road. The intersection of Longland Street and Doggett Street will change to prevent movements into Doggett Street. This will also prevent through movements from the Gasworks car park, at Longland Street. Traffic modelling indicates minimal increase in traffic volumes on local streets however, Council will monitor the local area following completion of the works to ensure the upgrade performs as anticipated. |
| Cycling facilities and connectivity | New on-road bike boxes are proposed on Commercial Road at the intersection to allow cyclists to move to the front of the lane when stopped at a red light. This will also increase awareness by providing a space where people riding a bike are clearly seen by all users at the intersection. Bike parking facilities are also being investigated and may be incorporated if safe storage areas can be found that do not impact the footpath area. |
| Australian Federal Police bollards | The Australian Federal Police (AFP) are planning to replace the existing temporary concrete barriers with steel bollards on the footpath in front of their building on the corner of Commercial Road and Doggett Street. This project is separate to the Council’s intersection upgrade. The timing for this work is yet to be finalised, however Council is working with the AFP to coordinate these works with the intersection upgrade. |
| Removal of on-street parking | To facilitate the upgrade and allow provision to extend the right-turn pockets, six parking bays on Commercial Road and four parking bays on Doggett Street will be removed. In addition, the Australia Post box on Commercial Road will be relocated approximately 80 metres east of the current location, and the loading zone on Commercial Road will be relocated approximately 20 metres west of the current location. |
| Impact to traffic flow | Changing Doggett Street to oneway will reduce the impacts of congestion at the Commercial Road intersection by eliminating one traffic phase. |

# COMMERCIAL ROAD AND DOGGETT STREET INTERSECTION

## NEWSTEAD

For more information about the project, please call the Project Team on 1800 669 416.

## Project timing

Detailed design

construction construction

early 2020

early 2020 mid 2020

## More information

To find out more about this project you can:

- phone 1800 884 681(business hours) or 3403 8888

- visit brisbane.qld.gov.au and search ‘Commercial Road and Doggett Street intersection upgrade’

- Write to Commercial Road and Doggett Street intersection upgrade project team:

City Projects

Brisbane City Council

GPO Box 1434

Brisbane Qld 4001